## Slide 1: ROS
Robot Operating System
Founded by Willow Garage and others,
Maintained and Developed by Open Robotics.

## Slide 2: What is ROS?
ROS is an open-source, meta-operating system(built on top of the operating system and allows different processes (nodes) to communicate with each other at runtime). It provides the services you would expect from an operating system.
Windows OS
BIOS

## Slide 3: How to use it?
Linux is used for running ROS. It is capable of running in many other OS too.
Terminal used to give commands and interact during runtime.

## Slide 4: WHY ROS over others?
The primary goal of ROS is to support code reuse in robotics research and development
ROS makes it easier to take advantage of a distributed computing environment
ROS is easy to integrate with other robot software frameworks.

## Slide 5
Each of them is a Node, which takes information from the sensor and processes it.
Is also a node which makes decisions based on the communicated information through topics or services in the form of messages.
Your text here
Analogous Example

## Slide 6: 1.SO how do they communicate? 2.How are they structured?

## Slide 7: ROS LEVELS of Concepts
ROS Computation Graph Level
ROS File System Level
ROS Community Level

## Slide 8: Ros computation graph
Nodes
Topics
Publisher
Subscriber
Services
Messages
Master

## Slide 9: nodes
S

## Slide 10: topics
Topics are named buses over which nodes exchange messages.

## Slide 11: Publisher and subscirber
Publisher: Node who sends information for others to access.
Subsciber: Node which receives information through the channel topic from the person who subscribed.

## Slide 12: messages
A message is a simple data structure, comprising typed fields. Standard primitive types (integer, floating point, boolean, etc.)

## Slide 13: Analogous example
Take youtube as an example
The person who uploads the video is publisher.
The channel you watch it is through youtube channel (the topic)
You subscribe to channel so you are the subscriber
The content you see is the in the form of videos (the message)

## Slide 15: Services
Request / reply is done via services, which are defined by a pair of message structures: one for the request and one for the reply.

## Slide 16: Actionlib
Services gives a information send and receive system
but for long processes you need the ability to stop it or
know about its progress. (Basically gives you more control)

## Slide 17: Why use services over topics
Topics are intended for unidirectional communication whereas, in complicated systems the concept of requesting and replying is required to know where the error might be arising from.

## Slide 18: master
The master acts as a name server for node-to-node connections and message communication. The command roscore is used to run the master, and if you run the master, you can register the name of each node and get information when needed.

## Slide 19: bags
Bags are a format for saving and playing back ROS message data.

## Slide 20: ROS File system level

## Slide 21: FILE system structure

## Slide 22: Packages
Packages are the main unit for organizing software in ROS
The goal of these packages it to provide this useful functionality in an easy-to-consume manner so that software can be easily reused. (Humans documented inventions to avoid reinventing and learning from the past)

## Slide 23: Workspace
A workspace is a set of directories (or folders) where you store related pieces of ROS code. The official name for workspaces in ROS is catkin workspaces.

## Slide 24: ROS Community
Distributions
Repositories
The ROS wiki
Bug Ticket System
Mailing List (updates, Q&A available)

## Slide 25: LETS CODE IT NoW !!!

## Slide 26: Our aim for today’s hands-on session
Revise file structure in ROS
Create workspace for our task
Task 1 : Making our own Package/Publisher/Subscriber
Task 2 : Understand ros msgs / Launch files through Husky Robot( ETH Zurich course)
- See how NASA , Clearpath and others use ROS
https://linklab-uva.github.io/autonomousracing/assets/files/L03.pdf

## Slide 27: Revise FILE system structure

## Slide 28: Revise filesystem
The main goal of the ROS Filesystem –
to CENTRALIZE the BUILD PROCESS of a project,
while at the same time provide enough flexibility and tooling to
DECENTRALIZE its DEPENDENCIES.

## Slide 29: Things related to Project developemen in ROS
Concept of Workspace( impt )
Catkin Workspace( info , structure)
Catkin , cmake , catkin make , why needed , how , where all can thses languages be used( not needed to run ROS projects but good to know)
Impt linux cmds (not specific to ros)
https://docs.google.com/document/d/1AhUAq8Xp5kavn6CNiLSMKcFCJZNqeEuUjtX7CnnVs5g/edit#
impt commands provided by ROS ( this is where ros comes into picture apart from internal commun btw files)
http://wiki.ros.org/ROS/CommandLineTools#rosnode

## Slide 30: Things related to Project developemen in ROS
Any ROS project begins with making a workspace.
In this workspace, you will put all the things related to this particular project.

## Slide 31: CATKIN

## Slide 32: Catkin Workspace
Modifications kept temp in build

## Slide 33: Quick note : What is Cmake?
CMake is an open-source, cross-platform family of tools designed to build, test and package software.
CMake generates these build files based on a set of configuration files, called CMakeLists.txt files, that describe the project's source code, dependencies, and build settings.
OpenCV
PCL
Qt
ReactOS
MySQL
Blender

## Slide 34
https://www.theconstructsim.com/what-is-the-construct/
Following along in
Either in your Ubuntu 20.04 with ROS Noetic
OR
The Construct Online E-learning Platform

## Slide 35: Task 1

## Slide 40: What WILL WE COVER
Intro to simple structure of node ( publisher and subscriber)
Info about turtlesim & turtlebot
Explaining a launch files, nodes, topics ,msgs through a simulated car(taken from a course work by ETH Zurich)

## Slide 41
Before we start coding!

## Slide 42: Functions provided by 2 of impt client libraries

## Slide 43: Nodes- Publisher(P)
Python node (P/S) can talk to cpp and vice versa but a single node can be written in only 1 language
Queue size

## Slide 44: SUbscriber

## Slide 47: Task 2 :
https://rsl.ethz.ch/education-students/lectures/ros.html

## Slide 49: Uses of ROS

## Slide 50: Astro bee
Three NASA Astrobee free-flying robots have been operating inside the International Space Station (ISS) since 2019. The astrobee packages consists of the flight software that runs onboard the Astrobee robots, a software simulator, and supporting tools, primarily written in C++.
- Three NASA Astrobee free-flying robots
Operating inside the International Space Station
(ISS) since 2019.
a software simulator and supporting tools,
primarily written in C++.
Astrobee's flight software performs
- vision-based localization
- autonomous navigation, docking, and perching,
supports human-robot interaction with co-located
astronauts via screen-based displays, sound, etc.
1.https://github.com/nasa/astrobee
ROS 2.https://www.nasa.gov/sites/default/files/atoms/files/fluckiger2018astrobee.pdf

## Slide 51: Robonaut 5
https://www.openrobotics.org/blog/2022/2/2/rosinspace
next generation humanoid, Robonaut 5 (R5), also known as Valkyrie.
R5's software was ROS-based from the beginning, and the team used Gazebo heavily in development and testing. NASA and R5 went on to compete in the DARPA Robotics Challenge (DRC).

## Slide 52: Clearpath robotics

## Slide 53: Industry Presence of ros
https://linklab-uva.github.io/autonomousracing/assets/files/L03.pdf
https://github.com/nasa/astrobee
Robot Operating System (ROS) framework as message-passing middleware.